## Slide 1
INTRODUCTION
스마트폰의 이용시간과 횟수의 증가는 현대인들의 근업 시간의 증가로 이어지게 되었으며 이로 인하여 안정피로 또한 증가하게 되어 자각적인 불편함을 호소하는 경우가 증가함
조절력의 감소를 나타내는 젊은 성인에서도 멀티포컬 렌즈의 처방 빈도가 증가하는 추세임[1-4]
이에 본 연구에서는 단초점 렌즈와 멀티포컬 렌즈를 각각 5일 씩 착용하여 착용 기간 동안의 조절기능의 변화와 렌즈 간 차이를 분석하고자 함
RESULTS
METHODS
안질환 및 전신질환이 없으며 단초점 렌즈와 높은 가입도의 멀티포컬 렌즈 착용 시 교정시력 0.8이상인 9명을 대상으로 함
A사 Air Optix 단초점 및 멀티포컬 렌즈(High addition)를 각각 5일 동안 착용하도록 함
조절기능과 관련하여 최대조절력, 양성상대조절, 음성상대조절, 조절래그를 40 cm거리에서 각 렌즈 착용 후 15분, 1일, 3일 및 5일이 경과한 후에 측정함
경시적 선형 혼합모형을 사용하여 착용기간에 따른 변화를 확인하였으며, 사후 분석을 통해 렌즈 간의 차이를 확인함
각각 착용기간에서 렌즈간 차이는 paired t-test를 이용하여 평가함
CONCLUSIONS
본 연구결과 높은 가입도의 멀티포컬 렌즈를 착용한 20대의 젊은 성인에서 근업 시 조절부담에 대한 긍정적인 변화가 확인됨
근업 시 조절피로 완화에 대한 긍정적 변화는 1일 이상 적응기간이 필요한 것으로 판단됨
멀티포컬 렌즈 착용 시 음성상대조절의 감소의 결과를 나타났으므로 조절이완이 힘든 조절과다의 경우 20대 성인의 멀티포컬 렌즈 처방 시 주의를 기울여야 할 것임
REFERENCES
2021 한국안광학회 동계학술대회
멀티포컬 소프트콘택트렌즈의 착용기간에 따른
20대 성인의 조절기능 변화
황인영 ∙ 김소라 ∙ 박미정*
서울과학기술대학교 안경광학과
[1] Korea optical news. Multifocal contact lens, rapid growth due to population aging, 2016. http://www.opticnews.co.kr/news/articleView.html?idx no=26569(7 September 2017)
[2] Mutti DO, Zadnik K. Is computer use a risk factor for myopia?. J Am Optom Assoc. 1996;67(9):521-530.
[3] Agarwal S, Goel D, Sharma A. Evaluation of the factors which contribute to the ocular complaints in computer users. J Clin Diagn Res. 2013;7(2):331-335.
[4] Thomson WD. Eye problems and visual display terminals the facts and the fallacies. Ophthalmic Physiol Opt. 1998;18(2):111-119.
Lens | AIR OPTIX AQUA Multifocal | AIR OPTIX AQUA PLUS HYDRAGLYDE
Manufacturer | Alcon | 
USAN+ | lotrafilcon B | 
Wearing schedule | 1 Month | 
Power(D) | +6.00D~-10D Low(~ + 1.25D) Mid(1.50D~2.00D) High(2.25D~2.50D) | +6.00D~-10D
Water contents(%) | 33 | 
Center thickness(mm) | 0.08 | 
Total diameter(mm) | 14.2 | 
Base curve(mm) | 8.6 | 
Lens design | Center near Bi-aspheric | Bi-aspheric
Table 1. The lens used in the study.
Fig. 1. Accommodation amplitude when wearing single vision- or multifocal contact lens for 5 days. (SV : single vision lens, MF : multifocal lens)
Accommodative amplitude (D) |  |  |  | 
Lens type | 15 min | 7 hour | 3 day | 5 day
SV | 11.32±2.05 | 11.13±1.99 | 10.97±2.30 | 11.16±2.10
MF | 11.97±2.51 | 10.45±1.89 | 11.69±2.19 | 11.34±2.75
P by paired t-test | .245 | .461 | .282 | .761
Mean ± SD SV : single vision lens, MF : multifocal lens |  |  |  | 
Table 2. Statistical analysis of accommodative ampli- tude with single vision- or multifocal contact lens wear.
Fig. 2. Positive relative accommodation with single vision- or multifocal contact lens wear (SV: single vision lens, MF: multifocal lens, PRA: positive relative accommodation)
Positive relative accommodation (D) |  |  |  | 
Lens type | 15 min | 7 hour | 3 day | 5 day
SV | -2.96±2.27 | -3.54±2.43 | -2.94±2.17 | -3.44±2.34
MF | -2.57±3.91 | -4.08±2.16 | -3.64±2.00 | -3.82±2.26
P by paired t-test | .836 | .339 | .138 | .165
Mean ± SD SV : single vision lens, MF : multifocal lens |  |  |  | 
Table 3. Statistical analysis of positive relative acco- mmodation with single vision- or multi- focal contact lens wear.
Chart: Wearing period(day)
| 0 | 1 | 3 | 5
SV | 11.3166 | 11.1299 | 10.9684 | 11.1593
MF | 11.9671 | 10.4513 | 11.6934 | 11.3362
Chart: Wearing period(day)
| 0 | 1 | 3 | 5
SV | -2.963 | -3.537 | -2.9444 | -3.4444
MF | -2.5741 | -4.0833 | -3.6389 | -3.8241
Chart: Wearing period(day)
| 0 | 1 | 3 | 5
SV | 2.4815 | 2.4167 | 2.5185 | 2.287
MF | 2.1852 | 2.1389 | 2.2685 | 2.3704
Fig. 3. Negative relative accommodation with single vision- or multifocal contact lens wear (SV: single vision lens, MF: multifocal lens, NRA: negative relative accommodation)
Negative relative accommodation (D) |  |  |  | 
Lens type | 15 min | 7 hour | 3 day | 5 day
SV | 2.48±0.81 | 2.42±0.88 | 2.52±0.74 | 2.29±0.63
MF | 2.19±0.61 | 2.14±0.74 | 2.27±0.78 | 2.37±0.40
P by paired t-test | .275 | .110 | .226 | .547
Mean ± SD SV : single vision lens, MF : multifocal lens |  |  |  | 
Table 4. Statistical analysis of negative relative acco- mmodation with single vision- or multifocal contact lens wear.
Chart: Wearing period(day)
| 0 | 1 | 3 | 5
SV | 0.48056 | 0.5187 | 0.48074 | 0.50556
MF | 0.87463 | 0.67574 | 0.80648 | 0.84815
Fig. 4. Accommodative lag when wearing single vision- or multifocal contact lens for 5 days. (SV : single vision lens, MF : multifocal lens)
Accommodative lag (D) |  |  |  | 
Lens type | 15 min | 7 hour | 3 day | 5 day
SV | 0.48±0.61 | 0.52±0.42 | 0.48±0.66 | 0.51±0.50
MF | 0.87±0.75 | 0.68±0.66 | 0.81±0.73 | 0.85±0.58
P by paired t-test | .035 | .371 | .204 | .114
Mean ± SD SV : single vision lens, MF : multifocal lens |  |  |  | 
Table 5. Statistical analysis of accommodative lag with single vision- or and multifocal contact lens wear.
멀티포컬 렌즈 착용 시, 최대조절력은 단초점 렌즈와 유의미한 차이가 없었고, 양성상대조절은 유의미한 증가, 음성상대조절은 감소가 나타남
멀티포컬 렌즈에서 높은 조절래그가 나타났으며, 각각의 구간을 비교한 결과 착용 15분 후 유의미한 차이가 확인됨